## Slide 1
Camera Calibration
Adam Hoover

## Slide 2
Outline
Coordinate systems
Intrinsic vs extrinsic parameters
Pinhole model
Radial lens distortion
CCD parameters
Tsai’s model
Calibration process
MATLAB toolbox
Riggs Sensor Network Lab

## Slide 3
Coordinate Systems
We seek to map points (Xw Yw Zw) in the world coordinate to points (X Y Z) in the camera coordinate system
Xw
Yw
Zw
X
Y
Z
camera image plane

## Slide 4
Camera Parameters (Extrinsic)
Extrinsic parameters describe camera location
Position
Orientation
X
Y
Z
T
R
translation vector (Tx Ty Tz)
rotation matrix (Rx Ry Rz)

## Slide 5
Camera Parameters (Intrinsic)
Intrinsic parameters describe physics of how camera senses the world
Lens can bend the light rays to increase field-of-view
Focal length imaginary point where light rays converge
CCD sensing element
light rays
focal point
lens
CCD

## Slide 6
Pinhole Camera (no lens)
All cameras see inverted data. The image is typically flipped during A/D.
A pinhole camera has a field-of-view proportional to its image size.
The light rays are all sensed along straight lines.

## Slide 7
Lensed Camera
A lens bends the light rays. They can bend inward or outward.
The field-of-view of is expanded (wide angle) or contracted (zoom) by the lens.
The focal length f manipulates the image size.

## Slide 8
Lens Parameters
Distortion at each pixel calculated as:
where
although k terms can be infinite, in practice only 1-2 terms are used
xu
xd

## Slide 9
CCD sensor
CCD sensors can vary in size (sensing area).

## Slide 10
CCD package
A CCD is an analog sensor, but is commonly packaged with A/D circuitry.

## Slide 11
CCD parameters
CCD parameters include:
Nx,Ny # sensor elements
dx,dy distance between elements
sx XY scale factor (if non-square)
Cx,Cy offset between lens and CCD
Nx
dx
center of lens
center of CCD
offset
(front view)
(side view)

## Slide 12
Tsai’s Camera Model
We use the extrinsic and intrinsic parameters to map points (Xw Yw Zw) in the world coordinate system to points (X Y Z) in the camera coordinate system.
Xw
Yw
Zw
X
Y
Z
Parameters:
Tx,Rx camera position/orientation
f focal length
k1,k2 lens distortion
sx XY scale factor (imperfections)
Cx,Cy offset between lens and CCD
Other models use less (pinhole) or more parameters depending on the application and precision needed in the mapping.

## Slide 13
camera image plane
Coordinate System Mapping
Xw
Yw
Zw
X
Y
Z
Step 1: world coordinates to camera coordinates
+T

## Slide 14
Coordinate System Mapping
Xw
Yw
Zw
X
Y
Z
Step 2: camera coordinates to ideal (undistorted) image coordinates
(X, Z)
image plane
(Xu, Zu)
f
(side view)
No “Z” in the image plane

## Slide 15
Coordinate System Mapping
Step 3: ideal image coordinates to distorted (by lens) coordinates
where
xu
xd

## Slide 16
Coordinate System Mapping
Step 4: distorted image coordinates to pixel coordinates
Nx
dx
(front view)
center of lens
center of CCD
offset
(side view)
where (Npx Npy) are number of pixels in the digital image
Upscaling (Nx Ny) to a larger (Npx Npy) creates the illusion of a larger image

## Slide 17
Calibration
Calibration uses a calibration target temporarily placed in the field-of-view.
The target has known dimensions and known world coordinates.
The target is constructed to simplify its segmentation during image processing.
Xw
Yw
Zw
X
Y
Z
(0,0)
(7,0)
(0,3)
4.8 cm
calibration target
origin of target coordinate system

## Slide 18
Targets
Checkerboard patterns are common because they are easy to segment.
1D patterns are sufficient, but 2D and 3D patterns can improve accuracy.
Filling the field-of-view improves estimates of lens distortion.

## Slide 19
Image Processing
We need image (col, row) to world (x, y) coordinate mappings.
Image processing can find these (semi-)automatically.
Assymetry on the target grid can help define the axes.
col,row = (703, 242)
x,y = (5.5, 0.5)
col,row = (356, 617)
x,y = (2.5, 5.5)

## Slide 20
Solving for Parameters
Equation solutions can be linear or nonlinear depending on model complexity.
Minimum number of mappings depends on number of model parameters.
In general, five or more mappings are bare minimum.
Output: parameter values
Tx,Rx camera position/orientation
f focal length
k1,k2 lens distortion
sx XY scale factor (imperfections)
Cx,Cy offset between lens and CCD
Input: list of image-to-world mappings
(col, row) (x, y)
(242,112) (0.5, 0.5)
(283, 116) (1.5, 0.5)
(331, 125) (2.5, 0.5)
… …
Set of equations describing camera model

## Slide 21
Visualizing Camera Model
Camera positions/orientations can be visualized relative to target.
This assumes the target did not move (the camera(s) moved).
Serves as a sanity check to detect errors during calibration process.

## Slide 22
MATLAB
Install the Computer Vision Toolbox.
Instructions for using the calibrator app.

## Slide 23
Riggs Sensor Network Lab
6 greyscale cameras
Computer and hardware in control room

## Slide 24
Riggs Sensor Network Lab
Custom calibration targets (poster boards)
Treat gently

## Slide 25
Riggs Sensor Network Lab
Custom software to capture image-to-world mappings and calibrate
Origin and axes identified manually per camera

## Slide 26
Tracking and Game Demo
Custom software to track people/objects moving around room
“Frog’s Revenge” virtual reality video game