## Slide 1
Device Drivers
Adam Hoover

## Slide 2
Interface between applications and hardware
Hardware interface
application
device driver
hardware

## Slide 3
standardized interface across different hardware
application developer does not need to worry about hardware details
device driver developer (manufacturer) insulates hardware
Software development
application
device driver
device driver
device driver

## Slide 4
all hardware treated like files
each piece of hardware gets its own filename
hardware accessed using file-like functions (open, read, etc.)
Design philosophy
/dev/hda
/dev/lp
/dev/usb1

## Slide 5
struct file_operations driver_fops = {
read(),
open(),
close(),
write(),
seek(),
…
}
Device driver functions
structure of function pointers
provided to O/S
application:
device driver developer writes a set of functions:
FILE *fpt;
fpt=fopen(“/dev/hda”, “r”);
driver_fops->open()
driver:
O/S

## Slide 6
struct file_operations driver_fops = {
read(), /* data transfer */
open(), /* setup */
close(), /* cleanup */
mmap(), /* provide access to driver memory */
ioctl(), /* control */
write(), /* data transfer */
seek(),
…
}
Device driver functions
device driver developer can put any code in any function
typically open/close handle setup/cleanup
typically read/write handle data transfer
ioctl (i/o control) is “handyman” for everything else

## Slide 7
O/S file management
-rw-r--r-- ahoover cuuser 6796 Sep 2 2019 index.html
normal file (ls -al):
brw-rw---- root disk 8, 0 Aug 24 2019 sda
brw-rw---- root disk 8, 1 Aug 24 2019 sda1
brw-rw---- root disk 8, 16 Aug 24 2019 sdb
brw-rw---- root disk 8, 17 Aug 24 2019 sdb1
crw-rw---- root disk 21, 0 Aug 24 2019 sg0
crw-rw---- root disk 21, 1 Aug 24 2019 sg1
device files (ls -al):
permissions
(user, group, all)
(read, write, exec)
owner
group
file size
(bytes)
last
mod
date
filename
driver file
b => block
c => character
major number
which set of functions to use
minor number
manage multiple copies

## Slide 8
Creating a device file
mknod –m660 /dev/sg0 c 21 0
crw-rw---- root disk 21, 0 Aug 24 2019 sg0
b => block
c => character
major
number
minor
number
To make a device filename, run the “mknod” command:
Device filenames can be removed using the standard “rm” command
permissions

## Slide 9
Providing driver code to O/S
make bzImage
/boot/vmlinuz.img
kgcc kernel.c
…
kgcc driver.c
…
Driver code can be compiled into the kernel:
The kernel file will contain the functions within “driver.c”
and be ready to use them upon booting.

## Slide 10
Dynamically add driver to O/S
gcc driver.c
driver.o
Driver code can be dynamically linked into the kernel:
The kernel can be updated with new code using the “insmod” command.
This can be done while the kernel is currently running.
insmod driver.o
(dynamically linked)

## Slide 11
O/S module management
insmod driver.o
module_init()
Driver developer writes functions for module insertion and removal:
These functions are included in the driver.c file.
rmmod driver.o
(setup, informs O/S
of major number)
module_exit()
(cleanup, removal)
lsmod
(see list of all modules currently linked and in use)

## Slide 12
struct file_operations driver_fops = {
read(), /* up to you */
open(), /* up to you */
close(), /* up to you */
mmap(), /* up to you */
ioctl(), /* up to you */
write(), /* up to you */
seek(), /* … */
…
}
Writing the driver
different for every piece of hardware
usually a mix of C and assembly
read spec sheet (manual) from manufacturer
provide useful interface to application developers

## Slide 13
Users and application developers all benefit from good device drivers.
When everything works correctly…